## Slide 1: Scenario of underground coal mining in India
Prof. R.M. Bhattacharjee

## Slide 2: Global coal production scenario
Coal provides around
  30.1% of global primary energy needs,
  generates over 40% of the world's electricity and is used in the production of 70% of the world's steel
Total Global Coal Production
  7823Mt (2013e)
  7794Mt (2012)
  4677Mt (1990)

## Slide 3: Top ten coal producing countries
PR China | 3561Mt | Russia | 347Mt
USA | 904Mt | South Africa | 256Mt
India | 613Mt | Germany | 191Mt
Indonesia | 489Mt | Poland | 143Mt
Australia | 459Mt | Kazakhstan | 120Mt

## Slide 4: Top ten steam coal producer
PR China | 3034Mt | Australia | 239Mt
USA | 756Mt | Russia | 201Mt
India | 526Mt | Kazakhstan | 103Mt
Indonesia | 486Mt | Colombia | 81Mt
South Africa | 255Mt | Poland | 65Mt

## Slide 5: Top ten coking coal producer
PR China | 527Mt | Canada | 34Mt
Australia | 158Mt | Mongolia | 20Mt
USA | 78Mt | Ukraine | 20Mt
Russia | 73Mt | Kazakhstan | 12Mt
India | 42Mt | Poland | 12Mt

## Slide 6: Top ten importers of coal
 | Total of which | Steam | Coking
PR China | 327Mt | 250Mt | 77Mt
Japan | 196Mt | 142Mt | 54Mt
India | 180Mt | 142Mt | 38Mt
South Korea | 126Mt | 95Mt | 31Mt
Chinese Tapei | 68Mt | 61Mt | 7Mt
Germany | 51Mt | 43Mt | 8Mt
UK | 50Mt | 44Mt | 6Mt

## Slide 7: Snapshots of Coal Production in India

## Slide 8: Trend of coal production in CIL mines since 1975

## Slide 9: Demand Supply Scenario in XI Plan

## Slide 12: Company wise coal production in XI Plan

## Slide 14: CIL Coal Production Programme – XII Plan Period

## Slide 15: Group wise coal production programme - CIL

## Slide 16: Underground coal production

## Slide 17: Technology wise production – CIL – XI Plan

## Slide 18: Technology wise production – SCCL – XI Plan

## Slide 19: Technology wise production – CIL – XII Plan

## Slide 20: Technology wise production – SCCL – XII Plan

## Slide 21: Reasons for decline in coal production from underground mines
UG operations at shallow depth has given way to quarry or surface mining
Reduced production and productivity due to old, long & arduous mines
Low technological, R&D or skill-development input in underground mines
Low productivity of manpower
Geological disposition and exploration of coal seams
Closure of number of underground mines due to exhaustion of coal reserve or losses
Reduction or stagnation in production due to attrition of workforce or natural retirement

## Slide 22: Reasons for decline in coal production from underground mines
Lower seams not approached – lack of vertical development
Limited coal evacuation capacity through shafts / inclines
Limited capacity of SDL / LHD for quantum jump of UG production
Lack of suitable mechanisation scheme
Mismatch of production components – drilling, blasting, loading, transportation, supporting, ventilation, communication
Lack of commitment towards high degree of mechanisation due to early history of failure of mass production technology
Lack of absorption of overseas technologies

## Slide 23: Reasons for decline in coal production from underground mines
Easy option of opencast coal – a challenge to underground production
Cost of production from opencast mining less compared to UG
UG mines are inherently more hazardous
Ease of mechanisation in opencast mines
Easy option of quantum jump of production by OC methods compared to UG methods
Difficulty in thick seam extraction by UG methods
Spontaneous heating propensity of Indian coal – high risk in UG mines
Lack of investment for infrastructure development and mechanisation resulting in capacity reduction

## Slide 24: Challenges of Underground Mining in CIL mines
Size of the Mine / block
Comparatively small size of mine or block with limited reserve restricting overall dimensions of a mine, thereby further constraining economic dimensions of mineable panels or coal sub-block, thus limits production capacity and life of the mine.
The mine/block area of most of the underground mines in CIL is generally less than 5sq. km.
Extractable reserve rarely exceeds 15-20Mt.
Its a challenge to plan and operate underground mine with capacity of 1.0Mt or more

## Slide 25: Challenges of Underground Mining in CIL mines
Geological Complexities and Exploration
multi-seam (upto 30 coal horizons),
seams thickness (upto 35m),
proximity of seams (parting <3m),
gradient (from flat to upto 45deg.),
quality of coal, low rank or maturity of coal, etc.
presence of structural disturbances, like multiple faults, occurrence of intrusive bodies, burning of coal, etc.
constrained economic dimension of working panels or coal sub-sub-blocks for mining.
The role of exploration is to facilitate complete exploration for delineation of all structures and other deposit attributes.

## Slide 26: Challenges of Underground Mining in CIL mines
Mine Approach & Development : high gestation period
Sluggish drivage of mine entries and mine development
Gestation period of about 6-12years to develop an underground mine.
Rates of drivages in underground are as low as 20-30m per month in stone/rock (single/twin roads) and about 30-60m per month in coal (two or more roadways).
No way near the rates achieved elsewhere in the world. It presents a challenge to match the international benchmark

## Slide 27: Challenges of Underground Mining in CIL mines
Technological Development & Implementation
Lack of Technological Innovation in ug mining
Problems in technology or operations being managed through in-house supportive efforts
Dependence on overseas technological
Delay in project implementation – cost over-run
Lack of standardisation of technology / equipment

## Slide 28: Challenges of Underground Mining in CIL mines
Absorption of Technology – Skill development
Indigenization of technology by suitable in-house manpower and skill development
Appropriate policies at corporate and operation level.
Upgrade and utilize trained persons at its appropriate and needed locations.

## Slide 29: Challenges of Underground Mining in CIL mines
Strata Management & Control
Strata management and control is most critical component of successful UG mining
Suitable strata management technology based on scientific assessment
Proper equipment
Trained manpower
Monitoring

## Slide 30: Challenges of Underground Mining in CIL mines
Mechanization – Productivity Enhancement Needs
Urgent need for mechanization of underground
Automation to minimize human effort and enhance productivity
Use of software to support technology management

## Slide 31: Strategy for improving UG Production in XII Plan
All new underground mines are to be planned with high degree of mechanization;
Large scale introduction of mass production technologies like longwall mining technology, continuous mining technology etc.
Non mechanized existing mines to be quickly converted to mechanised mines through adoption of SDL/LHD/Continuous miners and mechanized drilling and roof bolting;
In each subsidiary producing coal through UG operation, at least two high capacity UG mines are to be designed with state of the art technology, facilities of electronic monitoring, control system and facilities comparable to the best available in the world

## Slide 32: Strategy for improving UG Production in XII Plan
Scientific strata and environment monitoring;
Risk assessment and mitigation plans;
Faster development of infrastructure for UG mines- Mechanised shaft and incline drivages; high speed skips, conveyors etc.
Introduction of man riding systems in UG mines;
Adoption of telecommunications in underground mines;

## Slide 33: Current CM Projects
Subsidiary Company | No of mines | Name of the mines, CM Capacity (Mty)
ECL | 2 | Jhanjra (0.36) and Sarpi (0.46)
WCL | 2 | Tandsi(0.51)*
SECL | 4 | NCPH – Chirimiri(0.43), Sheetal Dhara – Kurja(0.36), Pinoura (0.48)and Rani – Atari(0.18)
Total CIL | 7 | Total Planned Capacity: 2.78 Mty

## Slide 34: Approved CM Projects in CIL
Subsidiary Company | No. of Mines | Name of Mines (Capacity, Mty)
ECL | 2 | Jhanjra 2nd CM(0.51); Kottadih(0.42)
BCCL | 1 | Block-II(0.45)
CCL | 3 | Chiri-Benti(0.84); Parej East(0.51); Piparwar- Mangardaha(0.61)
WCL | 5 | Dhankasa(0.91), Jamunia(0.45), Saoner-I(0.45), Tawa-II(0.36) & Gandhigram(0.78)
SECL | 5 | Churcha Re-organisation(1.02), Khairaha(0.49), Haldibari(0.30), Ketki(0.30) & Vijay (West)(0.30)
MCL | 3 | Talcher (West)(1.42), Natraj(1.15); Hirakhand Bundia Incline(0.42)
Total CIL | 19 | Total Planned Capacity: 11.69 Mty

## Slide 35: Potential Blocks for CM Project on Hiring basis
Subsidiary Company | No. of possible CMs | Name of Mines (Capacity, Mty)
ECL | 2 | Rangamati ‘B’ ( Kanchanpur Sector)
BCCL | 4 | Godhar ( Kusunda Area), AKW MC (Katras Area), Phularitand ( Barora Area) & Akash Kinari (Gobindpur Area)
CCL | 2 | Kalyani (Dhori Area) Mandu ( Hazaribag Area)
Total CIL | 8 | 

## Slide 36: Proposed Longwall projects of CIL
Sub. Company | Name of the Mines | Capacity (Mty)
BCCL | Moonidih XVI | 0.7
BCCL | Moonidih XV | 2.5
BCCL | Kapuria | 2.0
BCCL | Muraidih | 2.0
ECL | Jhanjra | 1.7
 | Total | 8.9