## Slide 2: Environmental effect of Marine Mining

## Slide 3: The impact of offshore mining will be resulted in the form of -
Plume at the sea floor.
Turbidity in the water columns
Addition of bottom sediments to the surface resulting in change in the marine eco system.
Adverse effect on marine life.
Destruction of benthic fauna of existing sea floor.

## Slide 4: According to estimates -
According to an estimate, an area of 300-600 sq km will be disturbed every year for mining of 3 million metric tones of nodules per year.
With every tonne of manganese nodule mined from seabed, 2.5-5.5 tonnes of sediment will be resuspended .
For an average 10,000 metric tonnes of nodules mined per day, about 40,000 metric tonnes of sediment will be disturbed (at 1 tonne nodule : 4 tonne sediment)

## Slide 5: As a result of such discharge -
The adjacent areas will not only have higher sedimentation rates, but the suspended loads may not only remain for over long periods but also travel laterally, causing clogging of filter feeding apparatus of benthic organisms in the area.
Sudden increase in the amount of suspended matter due to sediment plume and mining discharge, will increase the turbidity of these waters, and may also affect pelagic organisms
The debris and sediments mixed with water, which are lifted and transported with the minerals, will be discharged at the surface, and create turbidity. Their dispersion by currents will decrease the available sunlight for photosynthesis causing long term effects on biological productivity.

## Slide 6: Groups conducting environmental studies -
DOMES – Deep Ocean Mining Environment Study (1972-1981)
DISCOL - The DISturbance and Re-COLonisation (DISCOL) experiment was conducted by the scientists of the Hamburg University, Germany in the Peru Basin in the Pacific Ocean from 1988 to 1998.
NOAA-BIE - The benthic impact experiment (NOAA-BIE) by the National Oceanographic and Atmospheric Administration (NOAA, USA) was conducted in the Clarion Clipperton Fracture Zone (CCFZ) of the Pacific Ocean (1991 to 1993.
JET - The Japan deep-sea impact experiment (JET, 1994 - 1997) was conducted by MMAJ (Metal Mining Agency of Japan) in the CCFZ of the Pacific Ocean in 1994
INDEX - The Indian Deep-sea Environment Experiment (INDEX) was conducted by National Institute of Oceanography (Goa, India) in 1997 in a pre-selected area in the Central Indian Ocean Basin after a detailed baseline study from 1995-97

## Slide 7: Environmental factors must be considered to predict and control the negative impact of offshore mining
The proportion of total area that will be affected, with respect to total area of the water body.
Influence of surface and subsurface currents in different seasons
Distance of coastal belts and inhabited areas from the area of influence.
Existence of fishing potential or any other commercial activity in the area of influence.

## Slide 8: Precautions -
The separation of minerals from sediments (or other debris) should be as close as possible to the seabed, so that minimum water column is affected by the discharge.
Strip-wise mining to be carried out, leaving alternate strips of undisturbed seafloor, to allow re-population by organisms from adjoining areas.
The surface water discharge can be sprayed over a large area so that it can get diluted without much delay. Sediment discharge should be minimum at the surface, to allow sufficient sunlight to penetrate for photosynthetic activity.
Proper treatment of waste disposal to be carried out before discharging. Biodegradable methods should be used for treatment of discharge.