## Slide 1: www.MINEPORTAL.in
ONLINE TEST SERIES FOR
DGMS COAL/METAL FIRST/SECOND CLASS EXAM
GATE MINING EXAM
OVERMAN EXAM TEST
MINING INSPECTOR EXAMS
COAL INDIA MTs & OTHER PSUs EXAMS
FREE STUDY MATERIAL & VIDEO LECTURES
MINING JOBS NOTIFICATIONS
www.mineportal.in Call/Whatsapp-8804777500 www.fb.com/mineportal.in

## Slide 2: GPS RECEIVERS
Basically, a receiver obtains pseudo-range or carrier phase data to at least four satellites.
The type of receiver used will depend largely upon the requirements of the user. For instance, if GPS is to be used for absolute as well as relative positioning, then it is necessary to use pseudo-ranges.
If high-accuracy relative positioning were the requirement, then the carrier phase would be the observable involved.
For real-time pseudo-range positioning, the user’s receiver needs access to the navigation message (Broadcast Ephemerides).
If carrier phase observations are to be used, the data may be post-processed.
Most modern receivers are ‘all in view’, that is they have enough channels to track all visible satellites simultaneously.
A channel consists of the hardware and software necessary to track a satellite’s code and/or carrier phase measurement continuously.
When using the carrier phase observable, it is necessary to remove the modulations.
Modern geodetic receivers may work in a code correlation or codeless way. Code correlation uses a delay lock loop to maintain alignment with the incoming, satellite-generated signal.
The incoming signal is multiplied by its equivalent part of the generated signal, which has the effect of removing the codes.
It does still retain the navigation message and can therefore utilize the Broadcast Ephemeris.

## Slide 3
In the codeless mode a receiver uses signal squaring to multiply the received signal by itself, thereby doubling the frequency and removing the code modulation. This process, whilst reducing the signal-to-noise ratio, loses the navigation message.
Geodetic receivers used in engineering surveying may be single or dual frequency, with from 12 to 24 channels in order to track all the satellites available.
Some geodetic receivers also have channels available for GLONASS, the Russian system equivalent to GPS.
All modern receivers can acquire the L1 pseudo-range observable using a code correlation process.
When the pseudo-range is computed using the C/A code it can be removed from the signal in order to access the L1 carrier phase and the navigation message. These two observations could be classified as civilian data.
Dual frequency receivers also use code correlation to access the P code pseudo-range data and the L2 carrier phase.
However, this is only possible with the ‘permission’ of the US military who can prevent access to the P code. This process is called Anti-Spoofing (AS). When AS is operative a signal squaring technique may be used to access the L2 carrier.

## Slide 4
BASIC PRINCIPLE OF POSITION FIXING
Position fixing in three dimensions may involve the measurement of distance (or range) to at least three satellites whose X, Y and Z position is known, in order to define the user’s Xp, Yp and Zp position. In its simplest form, the satellite transmits a signal on which the time of its departure (tD) from the satellite is modulated. The receiver in turn notes the time of arrival (tA) of this time mark. Then the time which it took the signal to go from satellite to receiver is (tA − tD) = t called the delay time. The measured range R is obtained from
R1 = (tA − tD)c = t .c
where c = the velocity of light
Whilst the above describes the basic principle of range measurement, to achieve it one would require the receiver to have a clock as accurate as the satellite’s and perfectly synchronized with it.
As this would render the receiver impossibly expensive, a correlation procedure, using the pseudo-random binary codes (P or C/A), usually ‘C/A’, is adopted.
The signal from the satellite arrives at the receiver and triggers the receiver to commence generating its own internal copy of the C/A code.
The receiver-generated code is cross-correlated with the satellite code (as shown in the figure).
The ground receiver is then able to determine the time delay ( t) since it generated the same portion of the code received from the satellite.
However, whilst this eliminates the problem of the need for an expensive receiver clock, it does not eliminate the problem of exact synchronization of the two clocks.
Thus, the time difference between the two clocks, termed clock bias, results in an incorrect assessment of t.
The distances computed are therefore called ‘pseudo-ranges’.
The use of four satellites rather than three, however, can eliminate the effect of clock bias.
A line in space is defined by its difference in coordinates in an X, Y and Z system:

## Slide 5
If the error in R, due to clock bias, is δR and is constant throughout, then:
where Xn, Yn, Zn = the coordinates of satellites 1, 2, 3 and 4 (n = 1 to 4)
Xp, Yp, Zp = the coordinates required for point P
Rn = the measured ranges to the satellites
Solving the four equations for the four unknowns Xp, Yp, Zp and δR also solves for the error due to clock bias.
Correlation of the pseudo-binary codes

## Slide 6
Whilst the use of pseudo-range is sufficient for navigational purposes and constitutes the fundamental approach for which the system was designed, a much more accurate measurement of range is required for positioning in engineering surveying.
Measuring phase difference by means of the carrier wave in a manner analogous to EDM measurement does this.
As observational resolution is about 1% of the signal wavelength λ, the following table shows the reason for using the carrier waves; this is referred to as the carrier phase observable.
Carrier phase is the difference between the incoming satellite carrier signal and the phase of the constant frequency signal generated by the receiver.
It should be noted that the satellite carrier signal when it arrives at the receiver is different from that initially transmitted, because of the relative velocity between transmitter and receiver; this is the well-known Doppler effect.
The carrier phase therefore changes according to the continuously integrated Doppler shift of the incoming signal.

## Slide 7
This observable is biased by the unknown offset between the satellite and receiver clocks and represents the difference in range to the satellite at different times or epochs.
The carrier phase movement, although analogous to EDM measurement, is a one-way measuring system, and thus the number of whole wavelengths (N) at lock-on is missing; this is referred to as the integer or phase ambiguity.
The value of N can be obtained from GPS network adjustment or from double differencing or eliminated by triple differencing.
GPS OBSERVING METHODS
The use of GPS for positioning to varying degrees of accuracy, in situations ranging from dynamic (navigation) to static (control networks), has resulted in a wide variety of different field procedures using one or other of the basic observables.
Generally pseudo-range measurements are used for navigation, whilst the higher precision necessary in engineering surveys requires carrier frequency phase measurements.
The basic point positioning method used in navigation gives the X, Y, Z position to an accuracy of better than 20 m by observation to four satellites.
However, the introduction of Selective Availability (SA), see below, degraded this accuracy to 100 m or more and so led to the development of the more accurate differential technique.
In this technique the vector between two receivers (baseline) is obtained, i.e. the difference in coordinates (X, Y, Z). If one of the receivers is set up over a fixed station whose coordinates are known, then comparison with the observed coordinates enables the differences to be transmitted as corrections to the second receiver (rover).

## Slide 8
In this way, all the various GPS errors are lumped together in a single correction. At its simplest the corrections transmitted could be in a simple coordinate format, i.e. δX, δY, δZ, which are easy to apply.
Alternatively, the difference in coordinate position of the fixed station may be used to derive corrections to the ranges to the various satellites used.
The rover then applies those corrections to its own observations before computing its position.
The fundamental assumption in Differential GPS (DGPS) is that the errors within the area of survey would be identical. This assumption is acceptable for most engineering surveying where the areas involved are small compared with the distance to the satellites.
Where the area of survey becomes extensive this argument may not hold and a slightly different approach is used called Wide Area Differential GPS.
1. Static positioning
This method is used to give high precision over long baselines such as are used in geodetic control surveys.
At its simplest, one receiver is set up over a station of known X, Y, Z coordinates, preferably in the WGS84 reference system, whilst a second receiver occupies the station whose coordinates are required.
Observation times may vary from 45 min to several hours. This long observational time is necessary to allow a change in the relative receiver/satellite geometry in order to calculate the initial integer ambiguity terms.

## Slide 9
2. Rapid static
Rapid static surveying is ideal for many engineering surveys and is halfway between static and kinematic procedures.
The ‘master’ receiver is set up on a reference point and continuously tracks all visible satellites throughout the duration of the survey.
The ‘roving’ receiver visits each of the remaining points to be surveyed, but stays for just a few minutes, typically 2–10 min.
Using difference algorithms, the integer ambiguity terms are quickly resolved and position, relative to the reference point, obtained to sub-centimetre accuracy.
Each point is treated independently and as it is not necessary to maintain lock on the satellites, the roving receiver may be switched off whilst travelling between stations.
Apart from a saving in power, the necessity to maintain lock, which is very onerous in urban surveys, is removed.
This method is accurate and economic where there are many points to be surveyed.
3. Reoccupation
This technique is regarded as a third form of static surveying or as a pseudo-kinematic procedure.
It is based on repeating the survey after a time gap of one or two hours in order to make use of the change in receiver/satellite geometry to resolve the integer ambiguities.

## Slide 10
The master receiver is once again positioned over a known point, whilst the roving receiver visits the unknown points for a few minutes only.
After one or two hours, the roving receiver returns to the first unknown point and repeats the survey. There is no need to track the satellites whilst moving from point to point.
This technique therefore makes use of the first few epochs of data and the last few epochs that reflect the relative change in receiver/satellite geometry and so permit the ambiguities and coordinate differences to be resolved.
4. Kinematic positioning
The major problem with static GPS is the time required for an appreciable change in the satellite/receiver geometry so that the initial integer ambiguities can be resolved.
However, if the integer ambiguities could be resolved (and constrained in a least squares solution) prior to the survey, then a single epoch of data would be sufficient to obtain relative positioning to sub-centimetre accuracy.
This concept is the basis of kinematic surveying. It can be seen from this that, if the integer ambiguities are resolved initially and quickly, it will be necessary to keep lock on these satellites whilst moving the antenna.
4.1 Resolving the integer ambiguities
The process of resolving the integer ambiguities is called initialization and may be done by setting up both receivers at each end of a baseline whose coordinates are accurately known. In subsequent data processing, the coordinates are held fixed and the integers determined using only a single epoch of data.

## Slide 11
These values are now held fixed throughout the duration of the survey and coordinates estimated every epoch, provided there are no cycle slips.
The initial baseline may comprise points of known coordinates fixed from previous surveys, by static GPS just prior to the survey, or by transformation of points in a local coordinate system to WGS84.
4.2 Traditional kinematic surveying
Assuming the ambiguities have been resolved, a master receiver is positioned over a reference point of known coordinates and the roving receiver commences its movement along the route required.
As the movement is continuous, the observations take place at pre-set time intervals, often less than 1 s.
Lock must be maintained to at least four satellites, or re-established when lost. In this technique it is the trajectory of the rover that is surveyed and points are surveyed by time rather than position, hence linear detail such as roads, rivers, railways, etc., can be rapidly surveyed.
Antennae can be fitted to fast moving vehicles, or even bicycles, which can be driven along a road or path to obtain a three-dimensional profile.
4.3 Stop and go surveying
As the name implies, this kinematic technique is practically identical to the previous one, only in this case the rover stops at the point of detail or position required.

## Slide 12
The accent is therefore on individual points rather than a trajectory route, so data is collected only at those points. Lock must be maintained, though the data observed when moving is not necessarily recorded.
This method is ideal for engineering and topographic surveys.
4.4 Real-time kinematic (RTK)
The previous methods that have been described all require post-processing of the results. However, RTK provides the relative position to be determined instantaneously as the roving receiver occupies a position.
The essential difference is in the use of mobile data communication to transmit information from the reference point to the rover. Indeed, it is this procedure that imposes limitation due to the range over which the communication system can operate.
The system requires two receivers with only one positioned over a known point. A static period of initialization will be required before work can commence. If lock to the minimum number of satellites is lost then a further period of initialization will be required.
Therefore the surveyor should try to avoid working close to major obstructions to line of sight to the satellites. The base station transmits code and carrier phase data to the rover.
On-board data processing resolves the ambiguities and solves for a change in coordinate differences between roving and reference receivers.
This technique can use single or dual frequency receivers. Loss of lock can be regained by remaining static for a short time over a point of known position.

## Slide 13
4.5 Real-time kinematic on the fly
Throughout all the procedures described above, it can be seen that initialization or reinitialization can only be done with the receiver static.
This may be impossible in high accuracy hydrographic surveys or road profiling in a moving vehicle.
Ambiguity Resolution On the Fly (AROF) enables ambiguity resolution whilst the receiver is moving. The techniques require L1 and L2 observations from at least five satellites with a good geometry between the observer and the satellites.
There are also restrictions on the minimum periods of data collection and the presence of cycle slips. Both these limitations restrict this method of surveying to GPS friendly environments.
Depending on the level of ionospheric disturbances, the maximum range from the reference receiver to the rover for resolving ambiguities whilst the rover is in motion is about 10 km, with an achievable accuracy of 10–20 mm.