## Slide 2: Mining of Manganese nodules from sea floor

## Slide 3
Polymetallic nodules, also called manganese nodules, are rock concretions on the sea bottom formed of concentric layers of iron and manganese hydroxides around a core. The core may be microscopically small and is sometimes completely transformed into manganese minerals by crystallization. When visible to the naked eye, it can be a small test (shell) of a microfossil (radiolarian or foraminifer), a phosphatized shark tooth, basalt debris or even fragments of earlier nodules

## Slide 4
Nodules vary in size from tiny particles visible only under a microscope to large pellets more than 20 centimetres (8 in) across. However, most nodules are between 5 and 10 cm (2 and 4 in) in diameter, about the size of potatoes.
Their surface is generally smooth, sometimes rough, mammilated (knobby) or otherwise irregular. The bottom, buried in sediment, is generally rougher than the top.

## Slide 5: Development of mining system
Mining systems for deep-sea minerals (e.g. nodules) are based on the following three alternative concepts.
Hydraulic mining system: This system uses the principle of hydraulics in lifting the nodules. A collector mechanism is linked to the end of a pipe through which the nodules are lifted using pumps or compressed air injected into the pipe.
2. Continuous line bucket system: This system uses a chain of buckets driven along a line, which go down empty from the stern of the ship and come up partially filled after scooping the nodules from the sea-bed.

## Slide 6
3. Modular mining system : In this system, a self-propelled collector (shuttle) is launched with a ballast. As the shuttle moves on the seafloor, the nodules collected and the ballast is released on an equal weight on water basis. When mining is terminated, some more ballast is ejected; so the vehicle is slightly negative. The shuttle is propelled by thrusters, docked to the ship, unloaded and launched for mining.

## Slide 7: CONSIDERATIONS FOR NODULE MINING
Economic feasibility :-
The most important criterion for mining of nodule deposits is the non-availability of metals within a country and the cost of importing the metals from other countries. Supply and demand of these metals will determine the world and exploitation of offshore minerals will be considered economical when all other resources are exhausted to sustain industrial development. Hence, market trends for metals, such as Ni, Cu, Co, Mn and their non- availability will decide when deep-sea mining would begin.

## Slide 8
Delineation of mine-site:-`
The mine-site' is defined as an ocean bottom area where under specific geological, technical and economic conditions, a single mining operation can be carried out for a period of time. Several factors govern the selection of a manganese nodule mine site.

## Slide 9: THANK YOU